## Slide 1
Our World becomes digital
Thomas Marktscheffel, ASM Assembly Systems GmbH & Co. KG
Work Group: CFX – Hermes Report of Results from 2020 Meetings

## Slide 2: Participants of Workgroup “CFX - Hermes”
AEGIS Michael Ford
Arch Systems Tim Burke
ASM Tom Marktscheffel
Europlacer Alexis Fouquet
FlexLink Pat Ortiz
IPC Chris Jorgensen
Mycronic Håkan Sandell
Scheid IT Markus Scheid

## Slide 3: Objectives of Workgroup “CFX - Hermes”
IPC-HERMES-9852 provides horizontal communication, whereas IPC-2591 CFX provides vertical communication
Both Standards are complementary
Discussion in the Workgroup “CFX – Hermes” in 2020:
    How do Hermes and CFX interact at start of the SMT Line and at end of the SMT Line ?
    What about Sublines ?
    In-line removal and re-insertion of boards
    What about passing on subcircuit related information such as ink spots and barcodes ?

## Slide 4: Hermes – CFX Communication Overview
Place
Hermes Line
Inspect
Reflow
ExternalProcess
Supervisory System(s) / Hermes Line Manager
Hermes External
Panel
Hermes External
Panel
Hermes External Magazine
Hermes
External
Magazine
Conditional
Route
Insertion Event

## Slide 5: HERMES / CFX Identifiers
Overview of objects and identifiers used by CFX and Hermes standards
    CFX is using “Batch” to indicate a sub-group of work-order
    Hermes doesn’t differ between carrier and panels as only the one object is considered during the transfer between machines

## Slide 6: Workgroup “Hermes Use Cases”: Topics from Member Forum
The workorder concepts of Hermes and CFX are slightly different:
    Hermes does not have BatchId
    CFX.Production.Hermes.GetWorkOrderdata does not have Board Side, i.e. Hermes Flipped Board
Added Batch ID to related Messages, see Hermes Member Forum, November 2020
Added Flipped Board to CFX.Production.Hermes.GetWorkOrderdata – will be released with CFX 1.3

## Slide 7: Activities on Board Arrival at the Hermes Line
Single Board arrives  query work order information for board
    Use existing CFX.Production.Hermes.GetWorkOrderData message
Set of Boards arrives in a Magazine  query work order information for boards in the magazine
    New CFX.Production.Hermes.GetMagazineData message
      CFX.Production.Hermes.GetMagazineDataRequest MagazineId Identifier, e.g. Barcode of the Magazine
      CFX.Production.Hermes.GetMagazineDataResponse MagazineId Identifier, e.g. Barcode of the Magazine Units [] List of Boards contained in the Magazine • SlotId • <Hermes Board Data> Hermes BoardId, Top-/BottomBarcode, ProductTypeId, Width, WorkOrderIdentifier, …

## Slide 8: CFX – Hermes Interaction on Board Arrival at the Hermes Line
Query using board barcode
Query using workorder/batch
Query using magazine id
board barcode
board data object
Magazine id
Magazine object
Workorder/batch
Board data object (only product data)
CFX.Production.Hermes.GetWorkOrderData
Report magazine loaded
Magazine object
CFX.Production.Hermes.GetMagazineData
CFX.Production.Hermes.MagazineDeparted
CFX.Production.Hermes.MagazineArrived

## Slide 9: CFX – Hermes Reporting on Magazine Arrival and Departure
New CFX.Production.Hermes.MagazineArrived message to indicate arrival of a magazine
    MagazineId Identifier, e.g. Barcode of the Magazine
    Units [] List of Boards contained in the Magazine • SlotId • <Hermes Board Data> Hermes BoardId, Top-/BottomBarcode, ProductTypeId, Width, WorkOrderIdentifier, …
New CFX.Production.Hermes.MagazineDeparted to indicate departure of a magazine
    MagazineId Identifier, e.g. Barcode of the Magazine
    Units [] List of Boards contained in the Magazine • SlotId • <Hermes Board Data> Hermes BoardId, Top-/BottomBarcode, ProductTypeId, Width, WorkOrderIdentifier, …
Both messages will be released with CFX 1.3